## Slide 1: OSM-GB
Amir Pourabdollah
Jeremy Morley, Steven Feldman

## Slide 2: Some Research Questions
Will automated rules based processes improve quality?
Will formal QA increase confidence/authority?
Will improved QA & confidence & ease of access increase contribution?
Can “professional” contributors be “motivated” to fill in gaps?
What benefits arise from conflating OSM with Ordnance Survey data?
Notes: Apply rules based QI processes to OSM - identify possible errors & after some experiment automatically correct some errors. Enhance data through logical processes e.g. speed limits. Offer “improved” dataset back to the main OSM database (probably as a basis for further inspection prior to incorporation).
By making the data available via OGC WS, it is hoped that public sector users in CG & LG will be encouraged to experiment with OSM and identify potential use cases for OSM that are not met by current PSMA data.
Encourage prof users who have a great deal of local knowledge to become contributors to OSM. In the longer term it may even be possible to encourage these users to incorporate contributing to OSM as part of their routine workflows.
Explore win/wins with Ordnance Survey data – Open & Premium

## Slide 3: 3 Phases
Set up infrastructure and web services
Develop rules based improvements
& Public sector use cases
Explore conflation with OS OpenData

## Slide 4: Links and Communications
Central Government
  Ordnance Survey
  DEFRA
Councils
  Surrey Heath Borough Council
  Mole Valley District Council
  Warwickshire County Council
  Cambridgeshire County Council
Industry
  Astun Technology
  Cadcorp
  Snowflake
  Pitney Bowes
  Total Ren Solutions (serving Leicester City Council)
  Geolink Consulting
  ESRI
  TEP (Serving Home and Community Agency)
  OPTARK (Distribution Software Developer)
OSM Community
  Individuals
  OSM wiki
  OSMGB Blog and Twitter
Academic
  THE ISSUE Project
  Feedbacks from Lancaster University
  UoN School of Electrical Engineering (Mobile Network GIS)
  Through ELOGeo
Others
  National Trust
  OGC
  Feedbacks from Metropolitan Police
Overseas
  Committee for Geographic Names Australasia
  The University of Melbourne
  Delft University of Technology
  UoN Malaysian Campus

## Slide 5: System Design
Initial user group meeting + user discussions
Professional Users’ Requirements
  Raster and Vector Maps
  Coordinate Reference System
  OGC Compliance
  Consistent Access to National Open Maps
  Multiplicity of Layers
  Frequent Updates
  Quality Check and Fix
Orchestration between the available resources
  OSM ingestion
  Radius Studio
  Databases
  Open-source tools
  Web resources and open data

## Slide 6
Web
Services
WTMS
WMS
WFS
WMS-C
Client Side
Desktop GIS:
QGIS, ArcMap, ...
Web GIS:
OpenLayers, ...
OSM Editors:
JOSM, Potlatch, ...
Outside
OSM
OS Open Data
OSM Update
(Geofabrik)
OSM Community
Oracle Spatial
Server 1
Radius Studio
Workflow Engine
Web Interface
Web Services
Windows
Conversion Tool:
OGR2OGR
Server 3
Apache
Web Server
Tile Server
(renderd)
Mapnik OGCServer
Mapnik
Import Tools:
OSM2PGSQL
OSMOSIS
SHP2PGSQL
PostGIS
Linux
Server 2
GeoServer
GeoWeb
Cache
Apache Web Server
Linux
WordPress
WikiMedia
Python Script
Mapnik Style-sheet (XML)
PostGIS
Raster Maps
Infrastructure

## Slide 7: Daily (or Nightly) Update
Make backup +
Update raw OSM data
Transfer back processed data + Update OSMGB data
Transfer selected data + Process
Starts: 1:30 am
Lasts: 1 hour
Starts: 3 am
Lasts: 1.5 hour
Starts: 5 am
Lasts: 10 min
Server 3
Server 1+3
Server 1+3

## Slide 8: Optimized Update
Apply changes-only updates from OSM Replication Website (daily)
  Saves about 2hours daily
Apply rules/fixes on “selected” features instead of processing all OSM.
  All the buggy features from yesterday
    And all features in their proximity (currently 20m)
  Newly added/changed features
    And all features in their proximity (currently 20m)
  Saved time depends on rule-base (currently saving 2 days for each processing round)

## Slide 9
Start
Data Update Workflow
PostGIS
Oracle Spatial
Radius Studio: Apply
The rules
OSM Update
End
Linux Server
Windows Server
Export the “selected” features from PostGIS to Oracle
Update Changes
Apply the changes back to PostGIS
Data Backup
Revert Previous OSM-GB Changes
Data flow
Database
Task

## Slide 10: OGC Web Services
WMS
  Layers
    Land (5 sub-layers)
    Water (12 sub-layers)
    Buildings (7 sub-layers)
    Power (3 sub-layers)
    Boundaries (4 sub-layers)
    Transportation (38 sub-layers)
    Places (11 sub-layers)
    Amenities (6 sub-layers)
WMTS
    256x256 flatten tiles in png
WFS
    Separated by Points, Lines and Polygons
    Serving geometry + attributes
WMSC
    Quick WMS service (single layer)
WMS/WFS for Bugs
    Serving the detected bugs (Points, Lines and Polygons)
WFS for OS OpenData
  VMD (20 layers)
  Meridian-2 (19 layers)
CRS
  British National Grid (EPSG:27700)
  Lat/long (EPSG:4326)
  Google Mercator (EPSG:900913)
Vector Formats:
  GML 2, GML 3.1, GML 3.2, GeoJSON, ShapeFile and CSV
Raster Formats:
  png, pdf, kml, kmz, geotiff8, gif, jpeg, png8, svg, tiff, tiff
Tested on
  OpenLayers
  QGIS
  ArcMap
  Mapinfo
  Cadcorp

## Slide 11
Multi-layered WMS in Desktop GIS - ArcMap

## Slide 12
Using WMS/WFS in QGIS

## Slide 13
Using WMS/WFS in QGIS

## Slide 14
WFS for VMD
WFS for Meridian-2
WMS (OpenStreetMap)

## Slide 15
Waste collection points on top of MasterMap
Waste collection points on top of OSMGB WMS
Web Services; Professional Uptake
(thanks to James Rutter)

## Slide 16: RULES and BUG Detection

## Slide 17: Rules
Self Detection
  Geometry bugs - Topological inconsistencies
  Attribute bugs - Conceptual inconsistencies
  Geometry/Attribution bugs
  Mostly taken from KeepRight
  Listed in http://osmgb.org.uk/osm-gb-wiki/index.php/Quality_Improvement
OSM Community
  Non-standard attributes (taken from taginfo)
Differences with reference maps (OS VMD)
  Mismatched features
  Missing features

## Slide 18: Rule-base
Lines |  | 
Dead-ended one-way | 301 | 
Different-layer joint | 1466 | 
Geometry/Kickback | 404 | being fixed
Geometry/Spike | 1413 | being fixed
Intersection without junction | 36940 | 
Invalid motorway connection | 41 | 
Mismatched road name | 2427 | fixes - currently suspended
Mismatched road ref | 366 | fixes - currently suspended
Non-standard amenity tag | 419 | 
Non-standard building tag | 733 | 
Non-standard highway tag | 987 | 
Null road name | 1876 | being fixed
Null road ref | 1059 | being fixed
Overlapping roads | 637 | 
Self-intersected line | 22178 | 
Un-tagged bridge | 343 | 
Unclosed Area | 2651 | 
Wrong-level bridge | 646 | 
Wrong-level tunnel | 200 | 
Sum (19) | 75087 | 

## Slide 19: Rule-base – cont.
Polygons |  | 
Doubled place | 3317 | 
Geometry/Kickback | 34 | being fixed
Geometry/Spike | 1581 | being fixed
Non-standard amenity tag | 1931 | 
Non-standard building tag | 20510 | 
Non-standard highway tag | 5249 | 
Overlapping Buildings | 9736 | 
Ways intersecting Buildings | 6876 | 
Sum (8) | 49234 | 
Points |  | 
Non-standard amenity tag | 3706 | 
Non-standard building tag | 14865 | 
Non-standard highway tag | 3480 | 
Sum (3) | 22051 | 
Summary | 
OS Missing/Mismatches | 5728
Geometry autocorrections | 3432
Invalid geometry detection | 22178
Overlapping roads/buildings | 17249
Attribution issues | 7458
Road connection issues | 38447
Non-standard tags | 51880
Sum (30) | 146372

## Slide 20: Radius Studio Implementation
For All Rules
Oracle Spatial
(OSM, VMD, Standard Tags, etc.
Read Data
Check Rules Compliance
Apply action (Flag and/or Fix)
Commit Corrected tables
PostGIS

## Slide 21: Bug Layers

## Slide 22
Bug Layers (Fixed)

## Slide 23
Bug Layers (Not Fixed)

## Slide 24
In JOSM:
Bug layers for instant corrections

## Slide 25
Non-Standard tagging (?)
http://taginfo.openstreetmap.org/

## Slide 26
OSMGB:isbug tag

## Slide 27: OSM – OS Conflation

## Slide 28
VectorMap District
vs. Meridian-2
vs. OpenStreetMap

## Slide 29
VMD vs. OSM
Urban
Rural

## Slide 30
VMD vs. OSM: Update Delays

## Slide 31
VMD vs. OSM: Road Names

## Slide 32
VMD vs. OSM: Road Names

## Slide 33
VMD vs. OSM: Road Codes

## Slide 34
VMD vs. OSM: Road Codes

## Slide 35
VMD vs. OSM: Road Names/Code Differences

## Slide 36
VMD vs. OSM: Automatic Addition

## Slide 37
VMD vs. OSM: Flagging the Road Names Mismatches

## Slide 38: OS VMD Comparison
Mismatched road names
2471
Missing road names 2026
Missing road refs.
1121
Mismatched road refs.
377

## Slide 39: Patterns of road name bug ratios vs. road densities (20 x 20 km2)

## Slide 40: OSM Self-assessed Quality Researches

## Slide 41: OSM/OS Reference-based Quality Researches

## Slide 42: OSM Dynamicity Research
video link

## Slide 43: Publications so far
Journal:
  A. Pourabdollah, J. Morley, S. Feldman and M. Jackson: Towards an Authoritative OpenStreetMap: Conflating OSM and OS OpenData National Maps’ Road Network, submitted to the International Journal of Geo-Information, April 2013.
Booklet Article
  Amir Pourabdollah, Jeremy Morley, Suchith Anand and Mike Jackson, An Open GIS Case Study – OpenStreetMap for Great Britain (OSM-GB), submitted to THE ISSUE-NEREUS publication titled Space and ICT Applications supporting Smart, Green, Integrated Transport and Urban Mobility, May 2013.
Conferences:
  A. Pourabdollah, J. Morley, S. Feldman and M. Jackson, Studying the Dynamic Patterns of OpenStreetMap Bugs in Great Britain, the 16th AGILE Conference on Geographic Information Science, May 2013, Leuven, Belgium.
  A. Pourabdollah, J. Morley, S. Feldman and M. Jackson, OSM-GB: Using Open Source Geospatial Tools to Create OSM Web Services for Great Britain, accepted for FOSS4G 2013 conference, September 2013, Nottingham, UK.
  S. Feldman, A. Pourabdollah and J. Morley: OSM-GB - Can quality improvement increase contribution?, Society of Cartographers 48th Annual Conference, London, September 2012.
  J. Morley, A. Pourabdollah, T. Mooney, S. Feldman and M. Iliffe: Formalizing the Crowd - applying formal quality assurance processes to OpenStreetMap, AGI GeoCommunity ’12, Nottingham, September 2012.
Workshops:
  A. Pourabdollah and J. Morley, OSM-GB Workshop, the 4th Open-source GIS Conference, September 2012, Nottingham.
  A. Pourabdollah and J. Morley, OSM-GB Services and Data Workshop, accepted for FOSS4G 2013 conference, September 2013, Nottingham, UK.
MSc Thesis
  Chih-Yen Chang, Assessing the Data Quality of OpenStreetMap – An Examination of Overlapping Building in Great Britain, MSc in GIS, The University of Nottingham, 2012.

## Slide 44: Next steps
Longer term monitoring & detailed research
Recently incorporated new rules to examine tag consistency: are features tagged with recommended combinations
  Some argument from the OSM community about appropriateness of this check
Closing the feedback loop: tag “IsBug=no” to indicate a feature that is not in error
More community engagement for bug report checking & rules feedback

## Slide 45
www.osmgb.org.uk
www.nottingham.ac.uk/ngi
www.osm.org
Notes: Don’t forget to look at osmgb.org.uk